Open BLT Bootloader Configuration for Infinion XMC 4200

# Introduction:
Bootloader is the first piece of firmware which gets executed once the Embedded System is turned-on/reset. The primary objective of the Bootloader is to initialise the Embedded System and provide control to the Application/RTOS.
A bootloader is an application whose primary objective is to upgrade/modify system software without the intervention of specialized firmware upgrade tools. Bootloaders can have many functionalities, but it's mainly used to manage the application. They can also utilize different protocols such as UART, CAN, I2C, I2S, Ethernet, or USB to establish communication and initialize a firmware upgrade.
In general, the operation of a bootloader is relatively standard. There are three crucial parts in any bootloader: branching code, on startup, it decides whether to execute the bootloader code or the application code. This is done by checking a GPIO pin at start-up.
In a more complex system, the bootloader loads itself to the memory along with the application code, then it checks for initial parameters and system integrity. Once that's done, it goes back to executing the application code. This is why many bootloaders contain the branching code.
Even when the application is running, it's so designed that it can request a firmware upgrade, after which it takes care of the necessary system clean-ups once that is done, it soft-resets the chip by putting known values to the watchdog register. Additionally, the application puts out all the necessary instructions for the branching code to put the device on bootloader mode.
Now when the bootloader loads into the memory, it starts initializing basic instruction and peripherals to prepare for a firmware upgrade. The peripherals typically are system clocks, interrupts and communication channels, and schedulers. These allow the bootloader to accept instruction from outside, and it starts the upgrade process; once done, it soft-resets the chip, and when it boots up again, it goes to the normal operation mode.

# OpenBLT Bootloader:
OpenBLT is an open source bootloader that can run on any microcontroller and use any type of communication interface to perform software updates, without the need of specialized debugger hardware.
After the one-time integration of the bootloader into your microcontroller based product, the user or technician can work with the bootloader to conveniently perform a firmware update.
OpenBLT is mostly used as an STM32 bootloader, due to the popularity of STM32 microcontrollers. However, the bootloader’s architecture is such that it can work with any microcontroller. It currently supports ST STM32, Infineon XMC, NXP S12, and TI TM4C and LM3S microcontrollers. The source code organization creates a separation between microcontroller dependent and independent functionality, making it easy to port the bootloader to microcontroller targets that are not yet supported.
### Getting started:
The first step is to download OpenBLT. The latest version is available in the official feaser.com . The download package contains numerous preconfigured demonstration programs for popular microcontroller evaluation boards. You can either obtain one of these low-cost boards to first get familiar with operating the OpenBLT bootloader, or dive right in and port a demonstration program to your own hardware.
# Steps to flash the initial Bootloader:
## Program initialization:
Create the new simple project in the DAVE for the OpenBLT CAN bootloader

Figure 1 : Creating new Dave project

## Resource initialization:
Include the following files to the directory of the created new program
Sl no.	Required files
1.	blt_conf.h
2.	hooks.c
3.	led.c
4.	led.h
5.	shared_params.c
6.	shared_params.h
7.	main.c
8.	Source file

Open the properties of the new project file, go to the paths and symbols mention under the c/c++ general and add the path of the following files.
Sl no.	Files	Path of the files
1.	Source	${project name}/final_boot_main/Source
2.	ARMCM4_XMC4	${project name}/final_boot_main/Source/ARMCM4_XMC4
3.	GCC	${project name}/final_boot_main/Source/ARMCM4_XMC4/GCC

Figure 2 : Paths and Symbols window

Figure 3 :Adding path of the Directory

## OpenBLT configuration:
In the main bootloader project, the configuration file blt_conf.h is modified according to the CAN peripheral parameters because here we are mainly concentrating on the CAN bootloader.
Configure the values of the following macros in the file blt_conf.h , with the new mentioned value for the XMC 4200.
Sl no.	Macros	Value	Functionality
1.	BOOT_CPU_XTAL_SPEED_KHZ	12000	Frequency of the external crystal oscillator.
2.	BOOT_CPU_XTAL_SPEED_KHZ	80000	Desired system speed.
3.	BOOT_COM_CAN_ENABLE	1	Enable CAN transport layer.
4.	BOOT_COM_CAN_CHANNEL_INDEX	0	Select the desired CAN peripheral as a zero based index.
5.	BOOT_COM_RS232_ENABLE	0	disable UART transport layer.
6.	BOOT_COM_NET_ENABLE	0	disable the NET transport layer.
7.	BOOT_COM_NET_DEFERRED_INIT_ENABLE	0	disable the deferred initialization mechanism.
8.	BOOT_FILE_SYS_ENABLE	0	disable support for firmware updates from a locally attached storage.
9.	BOOT_FILE_LOGGING_ENABLE	0	disable logging messages during firmware updates.
10.	BOOT_FILE_ERROR_HOOK_ENABLE	0	disable a hook function that is called upon detection of an error.
11.	BOOT_FILE_STARTED_HOOK_ENABLE	0	disable a hook function that is called at the start of the update.
12.	BOOT_FILE_COMPLETED_HOOK_ENABLE	0	disable a hook function that is called at the end of the update.
13.	BOOT_NVM_CHECKSUM_HOOKS_ENABLE	0	disable hooks functions to override the user program checksum handling.
14.	BOOT_COP_HOOKS_ENABLE	0	disable the hook functions for controlling the watchdog.

Open the file led.c , this file is to validate the working of the bootloader , it has some function to initialize led to blink according to the time delay provided.

Figure 4 : Files to configure OpenBLT

In the led.c , we need to change the GPIO configuration according to considered pins.
## CAN peripheral configuration:
To configure the CAN peripheral open the main.c and configure the following values.
Sl no.	ports	pins
1.	Rx pin	14.3
2.	Tx pin	2.0

The next step is to change the CAN parameters in the same main.c file.
Sl no.	parameters	configuration
1.	CanModuleFreqHz	80MHz
2.	Can node	Node 0
3.	channel	Channel B

The can.c file is programmed to initialize the CAN peripheral of the XMC 4200 and a function is provided as can_init(); with the parameters required for the configuration of the CAN.

Figure 5 : main file to configure the CAN

Figure 6 : CAN parameters to be configured
## Port Specifics:
### Bootloader size
Due to the presence of the bootloader in the on-chip flash memory, the start address of the user program needs to be adjusted so make sure both programs do not overlap. Additionally, the bootloader's flash driver needs to be properly configured to prevent accidental erasure of the bootloader during firmware updates.
To reserve flash memory for the bootloader and protect it from being erased and/or reprogrammed during firmware updates, comment out lines in table flashLayout[] in source-file flash.c. Refer to the demo bootloader program for an example.
## Bootloader flash
Figure 7 : Bootloader flash sectors
Once after the completion of configuration all the files, Build the program and using the debugger flash the code into the memory of the microcontroller.
# Steps to configure the application program:
## Program initialization
Create the new simple project in the DAVE for the OpenBLT application project.
Refer the program initialization of the main program to create the project.

## Resources initialization
Include the following files in under the application project.
Sl no.	files
1.	boot.c
2.	boot.h
3.	shared_params.c
4.	shared_params.h
5.	header.h
6.	timer.c
7.	timer.h
8.	main.c

## CAN configuration
The CAN configuration should be done as the main bootloader program, open the boot.c file and the parameters should be configured according to main bootloader program.
Figure 8 : Application CAN configuration
## Port specifics
### Cheksum location
A 32-bit checksum value is programmed by the bootloader at the end of a programming session. Upon startup, the bootloader verifies the correctness of this checksum to determine if a valid user program is present and can be started. The user program must reserve space for this 32-bit checksum value in the startup file.
# Memory configuration
Figure 9 : Checksum location for OpenBLT
To load the application program to the memory of the microcontroller the linker file should be configured such as that the memory should exclude the reserved memory for the bootloader.
Figure 10 : linker script file

# Steps to flash the application program
## MicroBoot
The MicroBoot utility needs to be configured to connect to the correct CAN interface on the PC:
Start MicroBoot by double-clicking “\Host\MicroBoot.exe” .
Click the “Settings”-button and select “XCP on CAN” from the “Interface selection” dropdown box
Select the CAN communication device that your PC uses to connect to the CAN bus.
After building your application program, its S-record formatted firmware file can be downloaded to the remaining flash memory using the bootloader. In MicroBoot click the “Browse”-button and select your application program's firmware file.
Once the download completed, the newly programmed software will be started by the bootloader.

Figure 11 : Microboot interface